## Slide 1: Architecture & Design
Warehouse Robots – Team 3
Groep 3:
Jelle Claes
Nesim Dauwen
Maurice Vandenheede
Software Engineering for Cyber-Physical Systems 2025–2026

## Slide 2: Agenda
System overview
Robot architecture
  State machine
  Navigation & collision avoidance
  Hardware abstraction layer
Server architecture
  Task dispatch & aisle management
Communication (MQTT / REST / WebSocket)
Key design choices
Formal specifications (TLA+)
Conclusion & demo

## Slide 3: System Overview
Three independent tiers communicating over well-defined protocols
Robot tier (src/)
  State machine, navigation, collision avoidance, MQTT
  Platform-independent via abstract interfaces
  Event based system
  Scheduler
Server tier (server/)
  Task dispatch, aisle management, robot registry
  FastAPI REST API + WebSocket + MQTT broker
  Event based system
Web interface (webapp/)
  Real-time monitoring, task queue management via browser
  Vanilla JS, no build step, WebSocket-driven updates

## Slide 4: Robot Architecture – State Machine
8 states, each implementing on_enter / on_exit / update(dt) → TransitionID / on_event → None
  WAIT_CONNECTION → connects to MQTT broker
  IDLE → waits for task; requests aisle lock on task receipt
  WAIT_FOR_AISLE_ACCESS → halts; retries until lock granted
  MOVE_TO_AISLE → navigates to aisle entry point
  MOVE_TO_SEGMENT → navigates to shelf location
  PICK_ITEM → stops, waits 5–10 s (simulated pickup)
  MOVE_BACK_TO_AISLE → returns to entry; stops if lock lost (no retry)
  MOVE_TO_BASE → releases lock, publishes DONE, returns to base
Design choice: single responsibility per state → extensible & testable

## Slide 5: Navigation & Collision Avoidance
Proportional navigation (no PID)
  angular_vel = k_angular × angle_error
  linear_vel = k_linear × distance × cos(angle_error)
  Hard stop when |angle_error| > 0.8 rad → rotate in place first
  Arrival threshold: 0.02 m
LiDAR-based collision avoidance (CollisionManager)
  SAFE: path is clear → full speed
  EVADE: obstacle closing in → reduced speed + left-turn bias
  STOP: obstacle critically close → zero velocity + forced evasion window
Closing-rate detection: avoids unnecessary braking on stationary obstacles
  Collision applied per state via robot.collision.apply(linear, angular, dt)

## Slide 6: Hardware Abstraction & Platform Independence
Dependency Inversion Principle: robot depends on interfaces, not Webots
  IMotionController → move(linear, angular), stop()
  ISensorsController → get_scan(), get_front/left/right/rear_distance(), get_yaw(), get_gyro(), get_accelerometer(), get_wheel_positions()
WebotsHardware → low-level Webots device layer (motors, LiDAR, compass, IMU)
  WebotsMotionController and WebotsSensorsController both wrap WebotsHardware
  RobotFactory creates WebotsHardware and injects it into both controllers
Replacing WebotsHardware + both controllers is all that is needed for real hardware
  Robot core has zero Webots imports; factory reads robot ID and pose from customData

## Slide 7: Server Architecture
Task Dispatcher
  FIFO queue of pending tasks
  Nearest-idle-robot strategy → Euclidean distance to aisle entry
Aisle Manager – Mutual Exclusion
  Lease-based locking: one robot per aisle at a time
  Lease expires after 60 s → crash recovery without extra protocol
  On expiry: lock removed + robot notified (granted = false)
Robot Registry & Tracker
  Auto-register on first heartbeat → no pre-configuration
  OFFLINE if no heartbeat for 4 s; OFFLINE state not cleared by heartbeat

## Slide 8: Communication Architecture
MQTT (QoS = 1, JSON payloads)
  robot/{id}/heartbeat Robot → Server every 0.5 s
  robot/{id}/task/assign Server → Robot
  robot/{id}/task/status Robot → Server
  robot/{id}/aisle/response Server → Robot
  aisle/{id}/request|release Robot → Server
REST API (FastAPI)
  POST /api/tasks → submit task | DELETE → cancel PENDING
  GET /api/robots, /api/tasks, /api/aisles → current state
WebSocket /ws
  Server-push: robot_heartbeat, task_status, aisle_request/release
  Eliminates polling; UI updated in real time

## Slide 9: Key Design Choices
State machine
  Single responsibility per state; extensible without modifying existing states
Abstract interfaces + factory (DIP)
  Robot core has zero Webots imports; swap hardware layer for real hardware
MQTT pub-sub
  QoS=1 handles WiFi dead spots; wildcard topics scale to N robots
Lease-based aisle locking
  Simple crash recovery; no extra heartbeat or acknowledgment needed
Closing-rate collision detection
  Distinguishes moving from stationary obstacles; avoids unnecessary braking

## Slide 10: Key Design Choices
Thread-safe EventQueue
  Keeps state machine single-threaded; only shared structure with MQTT thread
Nearest-idle-robot dispatch
  O(n) simplicity; encapsulated in one method; trivially replaceable

## Slide 11: Formal Specifications (TLA+)
Three TLA+ modules capture the key safety and liveness properties
AisleMutualExclusion
  MutualExclusion: at most one robot holds any aisle lock
  ExpireLease: models the 60 s server-side timeout
RobotStateMachine
  NeverEnterWithoutLock: robot never navigates in aisle without the lock
  TaskEventuallyDone: every assigned task eventually completes (liveness)
TaskLifecycle
  SingleAssignment: a task is assigned to at most one robot
  NoRollback: DONE and REJECTED are terminal states

## Slide 12: Conclusion
Clean three-tier separation: robot, server, web interface
Robot code is fully platform-independent
  WebotsHardware + two controllers are the only Webots coupling
Lightweight coordination mechanisms on the server
  Lease-based aisle locking handles crashes without extra protocol
  Nearest-robot dispatch is simple, correct, and replaceable
Design deliberately favours simplicity over premature optimisation
  Proportional nav, closing-rate collision, greedy dispatch
  Each choice is behind an interface or a single method
Solid proof-of-concept ready for real-hardware deployment

## Slide 13: Demo & Questions
Live demonstration of the Warehouse Robots system
Groep 3: Jelle Claes | Nesim Dauwen | Maurice Vandenheede